## Slide 1: Myanmar: Towards Universal Access to Electricity by 2030
Nay Pyi Taw, January 28, 2015
Notes: 1

## Slide 2
A Bridge to a Sustainable Energy Future
A Bridge to Universal Energy Access
National Electrification Plan towards Universal Access by 2030:
Some Key Messages
Notes: In collaboration with State Department

## Slide 3
20
Note: This map shows all settlement points the same size (regardless of population), overstating electrification with non-grid options (mini-grid and off-grid / solar home systems)
Least-cost recommendation for 2030
By 2030, the majority are grid connections
This represents 7.2 million households
Total cost is estimated at US $5.8 billion (US$800 per connection, average)
This is additional to investments needed for generation & transmission

## Slide 4
Roadmap to Achieve Universal Access by 2030
After 2019, over 517,000 connections have to be made each year to reach full electrification by 2030
National Electrification Rate
33%
47%
76%
100%

## Slide 5
Chart: 
| 2012 | For universal electrification by 2030
No. of new connections per year | 59000 | 440000
 | 130000
Source: MOEP (2011-2012), ESE, YESB data and Castalia estimations
Assumes 6.5 people in a household
 | ESE
 | YESB
 | Required
189,000
New household connections per year
Need to connect over 2x as many households per year to reach universal electrification by 2030…
Myanmar’s electrification challenge is immense…
The electrification rate is estimated at 33%...

## Slide 6
Recommended Sequencing of Grid Roll-out proceeds from low-cost to high-cost connections
Dense areas require shorter distribution lines and lower cost per connection and will be connected first
Remote communities require longer lines and higher cost and will be connected later
Chin, Shan, Kachin and Kayah have highest cost per connection, thus to be connected in the final phases
Connected earlier
Connected later

## Slide 7
3-4% of the villages in the last phases of grid rollout are recommended for pre-electrification
Pre-electrification villages shown in purple
Shan, Chin, Kayah and Kachin States represent major areas for pre-electrification
Recommendations for off-grid pre-electrification
Notes: For those areas where grid will arrive late, an off-grid “pre-electrification” option can provide non-grid electricity service in the short- and medium-term

## Slide 8
Solar home systems for smaller villages (<50 households)
  may provide 75-175 kWh/yr for lighting/phones/TV
  US $400-500 per household
    (These are international prices with good quality. Local prices may be lower, and quality can vary.)
Mini-grids for larger villages (>50 households)
  solar, hybrid, diesel, or micro-hydro where available
  200-250 kWh/yr : lighting/ICT/TV & fan/small fridge
  US$1,400/HH
  Could be integrated to grid later, and save on distribution investment, if built to grid standard
Appropriate pre-electrification technology depends on village size

## Slide 9
Institutional recommendations
YESB Franchise Area
Develop investment program with IFC
Corporatize YESB
ESE Franchise Area
Follow YESB path
Set up sub-franchise concessions
Mini-grid connections
DRD manage & monitor
Decentralized, standard approach modeled on ESE sub-franchise concessions
Off grid connections
DRD manage & monitor
Re-orient to financial incentives rather than free solar home systems
Support private sector provision
Private Sector
▪ Participate in sub franchise concessions ▪ Provide solar home systems
Executive Secretariat reporting to VP Office
Overall management and coordination of geospatial plan
Performance reporting
Point source for donors
Donors
TA to establish and train new entities
Concessional finance
Establish loan program with banks
Under MOEP leadership
Independent Regulator
Advise on tariffs, standards and subsidies needed

## Slide 10
From Plan
To
Action

## Slide 11
A Bridge to Universal Energy Access
  Help increase access to electricity in Myanmar
  with $300-400 million IDA credits
  - Expected outcomes include:
    New household connections in urban and rural areas
    Coordinated, sector-wide institutional framework for electrification
    Strengthened institutional capacity of implementing agencies
National Electrification Project: Objectives

## Slide 12
A Bridge to Universal Energy Access
  Component 1: Grid rollout (US$ 200 – 300 million)
  For extension of distribution lines operated by ESE and YESB and connections of villages and households.
  Component 2: Off-grid pre-electrification (US$ 80 million)
  For mini-grids and household systems in remote villages unlikely to connect to the grid in the next 8-10 years. Includes:
  solar photovoltaic (PV) systems
  mini-hydropower (< 1 MW)
  Wind, diesel and hybrid systems (e.g. diesel/solar).
National Electrification Project: Proposed Components

## Slide 13
A Bridge to Universal Energy Access
Component 3: Capacity building and technical assistance (US$ 20 million)
For support to Government agencies (union, state/ region, district) and private sector to plan, implement, monitor and evaluate the NEP. Includes:
  technical design
  economic and financial analysis
  environmental and social impact management
  procurement and financial management.
Component 4: Contingent Emergency Response (US$ 0 million)
For a fast re-allocation of finance in case of natural disaster.
National Electrification Project- Proposed Components

## Slide 14
A Bridge to Universal Energy Access
Priority Investment Activities for Grid Extension based on National Electrification Plan
States/Regions | # Townships | # Villages | # HHs
Ayerwaddy | 26 | 704 | 77,901
Bago(East) | 14 | 558 | 76,523
Bago(West) | 14 | 784 | 73,382
Chin | 4 | 13 | 1,141
Kachin | 10 | 180 | 29,112
Kayah | 3 | 39 | 1,762
Kayin | 3 | 87 | 9,114
Magway | 12 | 227 | 32,503
Mandalay | 20 | 680 | 99,531
Mon | 7 | 96 | 15,915
Nyapitaw | 8 | 170 | 34,704
Rakhine | No data | No data | No data
Sagaing | 30 | 733 | 99,818
Shan(East) | 2 | 4 | 210
Shan(North) | 1 | 3 | 154
Shan(South) | 18 | 290 | 28,113
Tanintharyi | 7 | 24 | 5,700
Grand Total | 179 | 4,592 | 585,583

## Slide 15
A Bridge to Universal Energy Access
Priority Investment Activities for Off-Grid Electrification based on National Electrification Plan
 |  | Solar Home Systems |  | Mini-Hydro | 
States/Regions | # Townships | # Villages | # HHs | # Villages | # HHs
Ayearwaddy | 3 | 12 | 2,668 | - | -
Bago(East) |  |  |  |  | 
Bago(West) |  |  |  |  | 
Chin | 9 | 115 | 5,344 | 10 | 793
Kachin | 3 | 28 | 4,000 | - | -
Kayah | 3 | 15 | 750 |  | 
Kayin | 2 | 62 | 3,333 | - | -
Magway |  |  |  |  | 
Mandalay |  |  |  |  | 
Mon |  |  |  |  | 
Nyapitaw |  |  |  |  | 
Rakhine |  |  |  |  | 
Sagaing |  |  |  |  | 
Shan(East) | 9 | 108 | 5,298 | 3 | 821
Shan(North) | 8 | 66 | 4,000 | 1 | 600
Shan(South) | 5 | 41 | 4,000 | 2 | 600
Tanintharyi |  |  |  |  | 
Grand Total | 42 | 447 | 29,393 | 16 | 2,814

## Slide 16
A Bridge to Universal Energy Access
Project Institutional Implementation Framework

## Slide 17
A Bridge to Universal Energy Access
Project Preparation Schedule
Milestone | Date
World Bank approves project concept | November 2014
Consultative meeting with civil society | January 2015
Parliament approves project request | March 2015
Public consultation on draft Environment and Social Management Framework | May 2015
World Bank Board of Directors approves project | July 2015
Project implementation begins | September 2015

## Slide 18
A Bridge to Universal Energy Access
NEP reports and project materials can be found at:
https://energypedia.info/wiki/ Achieving_Universal_Access_to_Electricity_in_Myanmar
Discussions and Q&As